## Slide 1: MPLS 101
MPLS and VPLS fundamentals
Nick Buraglio
http://www.forwardingplane.net/
6/6/2013

## Slide 2: Purpose and Scope
The purpose of this slide deck is to be a bootstrap and reference for terminology and concepts for the umbrella suite of protocols within MPLS
It is not meant to be an operational guide or to be a definitive resource but instead a compilation of a superset of references condensed into a portable, convenient format

## Slide 3: Overview
MPLS is broken up into transport and services.
  L3VPN
  L2VPN
  VPLS
MPLS as a transport is plumbing for the MPLS service to utilize.

## Slide 4: Concepts - MPLS
Label Switching
  Utilizes labels to switch much faster than layer 3 routing
  Happens at data link layer
  Similar to ATM and Frame Relay, which both use label switching at their core
  Permits finer granularity resource allocation to traffic streams
  MPLS is an open standard (RFC 3031)
Notes: L3 routing has increased in speed of table lookups since the inception of MPLS. Conceptually similar to ATM and FR. Format of labels is reminiscent of BGP communities. Allows for very granular control of traffic paths. Is an open standard.

## Slide 5: Concepts - MPLS
Label Switching is similar to:
  BGP communities (in format)
  Frame Relay DLCI
  ATM VPI/VCI

## Slide 6: Concepts - MPLS
MPLS
  Locates shortest paths based on labels rather than longest network match
  Avoids lookups in routing table
  Labels identify virtual links as opposed to endpoints
  Data Link layer agnostic. MPLS can function over ATM, Ethernet, Frame Relay, SONET, etc.
  More like switching than routing
  Sometimes referred to as layer 2.5
  Packet switching technology

## Slide 7: Concepts - MPLS
MPLS
  Lookups happen in the switch fabric rather than the CPU
  Creates a faster lookup time and lower hardware overhead*
        *RIB lookups are significantly faster then they were at the inception of MPLS
Notes: Juniper PTX is a good example of lower hardware overhead. The PTX has very little memory for routing table and is meant to be a label switching core device.

## Slide 8: Functionality
MPLS
  Only necessary to do one IP lookup
    Lookup occurs when the packet first enters the MPLS domain for the duration of the transit of the packet
    Lookup for the last hop
  Adds a prefix to packets with an MPLS header, containing one or more labels called a label stack

## Slide 9: Functionality
  Each label stack entry contains four fields:
    A 20-bit label value.
    A 3-bit Traffic Class field for Quality of Service (QoS) priority (experimental) and Explicit Congestion Notification (ECN)
    A 1-bit bottom of stack flag. If this is set, it signifies that the current label is the last in the stack
    An 8-bit time to live field

## Slide 10: Functionality
MPLS Header
Notes:     20-bit label value, 3-bit Traffic Class field for Quality of Service (QoS) priority (experimental) and Explicit Congestion Notification (ECN), A 1-bit bottom of stack flag. If this is set, it signifies that the current label is the last in the stack, An 8-bit time to live field

## Slide 11: Terminology
LSP – Label switched path (similar to PVC in ATM but not dependent on L2 technologies)
PE – Provider Edge Router
  Sometimes referred to as Label Edge Router (LER)
P Router – routers that function specifically as transit devices
  P routers simply transit traffic and can be significantly less complicated and robust*
  Also known as the Label Switch Router (LSR)
CE – Customer Edge device.
  Last hop into customer network
  Generally not MPLS aware
Notes: Multiple names for everything. In my experience most common references are PE, P and CE

## Slide 12: Terminology
LIB – Label information base
  Software table maintained by each router for storage of learned and local port and corresponding label to be popped or pushed on incoming or outgoing packets
  Used by label distribution protocol (LDP)
  Used by LDP for mapping next hops
  Is a function of the MPLS control plane

## Slide 13: Terminology
LFIB - Label Forwarding Information Base
  FIB for MPLS label forwarding
  Used for managing forwarding in which destinations and incoming labels are associated with outgoing interfaces and labels
Notes: Maps an incoming label to a destination interface

## Slide 14: Terminology
P Router / LSR – Label switch router
  Routers that perform routing based only on the label
PE Router / LER – Label Edge Router
  The entry and exit points of an MPLS network
  push an MPLS label onto an incoming packet and pop it off the outgoing packet
Notes: P router has limited to no routing
PE router is the ingress and egress of an MPLS network. Will discuss “push” and “pop” on next slide

## Slide 15: Terminology
LDP – Label Distribution Protocol
  Protocol for distribution of labels between LERs and LSRs
Label swap
Label push (impose)
Label pop (dispose)
pseudo-wire (PW, VLL)
  An emulation of a point-to-point connection over a packet switched network
Notes: Pseudo-wire is most common term. VLL is brocade term. Acts as a long patch cable, garbage in, garbage out. Very little intelligence. Can be tagged or untagged. LDP most comonly used in smaller networks. Very simple.

## Slide 16: Terminology
LDP
  Uses UDP multicast 224.0.0.2:646 to discover neighbors
  Uses TCP port 646 once neighbors are discovered
  Requires IGP (ISIS, OSPFv2, OSPFv3) to function
  Advertises labels for IGP learned routes
  Routers running MPLS distribute their labels for each prefix to their neighbors
  Each router only knows about its neighbor’s labels
    Each router does not have a full view of the network
Notes: Uses multicast group for discovery like OSPF. Needs to have a functional IGP to work. Build interconnect, bring up loopbacks, then enable IGP. Then bring up LDP using loopbacks

## Slide 17: Terminology
RSVP - Resource Reservation Protocol
  Transport layer protocol for reservation of resources across a network
  Operates over IPv4 and IPv6
  Does not transport application data
  Similar to a control protocol like ICMP or IGMP
  Can be used to request or or deliver QoS for data streams or flows
  RSVP-TE is more common today and is an extension of RSVP

## Slide 18: Terminology
RSVP-TE - Resource Reservation Protocol - Traffic Engineering
  Extension of the RSVP protocol for the purpose of traffic engineering
  Supports reservation of resources over an IP based network
  Allows for the establishment of LSPs taking into consideration network constraint parameters such as available bandwidth and explicit hops
  Operationally RSVP-TE is more more robust and scalable

## Slide 19: Terminology
RSVP-TE
  Operationally RSVP-TE is more more robust and scalable than LDP
  Operational complexity can be higher with RSVP-TE due to it’s more feature rich nature

## Slide 20: Terminology
FEC – Forwarding equivalent class
  Characteristics for determining the FEC of a higher-layer packet
  Depend on the configuration of the router
  Typically this is the destination IP address at a minimum
  Quality of service class is also often used.
  A Forward Equivalence Class generally corresponds to a label switched path (LSP)
  The reverse is not normally true
  LSPs may be (and usually are) used for multiple FECs

## Slide 21: Functionality
Topmost label is examined when a packet enters an LSR
Actions based on topmost label and pre-built tables allow for very fast operations
Labels may have pre-built label tables
Label is inserted between the Layer 2 header and the Layer 3 header

## Slide 22: Operation
Label Operation
  Label Push – adds a label to incoming packet; also called label imposition
  Label Swap – replaces the label on an incoming packet
  Label Pop – removes the label on an outgoing packet; also called label disposition
  Penultimate Hop Popping (PHP)
    Without PHP, the egress PE router must perform two lookups. First it has lookup the destination prefix associated with the label, and then once it has the prefix; the router must look up the next-hop for the destination prefix. With PHP, the next-to-last hop router (the penultimate router) will perform the label pop operation. This means the egress PE router will not have to do the label lookup because it is receiving an IP packet (the penultimate router has popped the label off before forwarding it to the egress router).

## Slide 23: VPLS

## Slide 24: Concepts - VPLS
VPLS - Virtual Private LAN Service
  Also called L2VPN
  Is a mechanism for providing Ethernet based multipoint to multipoint communication over IP/MPLS networks
  Allows for any-to-any connectivity

## Slide 25: Concepts - VPLS
  In a VPLS environment the LAN in question at each site is extended to the edge of the provider network
Service provider network (SP) emulates a bridge / switch to create a single bridged network
Designed for applications that require multipoint or broadcast access

## Slide 26: Functionality - VPLS
VPLS emulates a LAN, full mesh connectivity is required between all devices
Two methods for full mesh establishment for VPLS
  BGP
    Provides auto discovery as well as signaling
  LDP

## Slide 27: Functionality – VPLS
VPLS MPLS packets have a two-label stack
  Outer label used for normal MPLS forwarding within the service provider's network
  If BGP signaled, the inner label is allocated by a PE as part of a label block
  If LDP signaled, the inner label is a virtual circuit ID assigned by LDP when mesh is first established between participating PEs.
  Every PE keeps track of assigned inner label, and associates these labels with the VPLS instance.

## Slide 28: Functionality – VPLS
VPLS requires a full mesh in both the control and data planes
  BGP better for large scale due to better scaling utilizing route reflectors
  Scaling LDP over a large amounts of VPLS sites generally uses a hierarchical design (HVPLS)

## Slide 29: Use Cases
Transparent tunneling over existing networks
BGP free core
Layer2 VPN services
Layer3 VPN services

## Slide 30: Use Cases
Traffic Engineering
  Redistribution of traffic load over underutilized links
  Bandwidth guarantees / CIR
  Fast failure recovery

## Slide 31: References
http://networkstatic.net/juniper-and-cisco-comparisons-of-rib-lib-fib-and-lfib-tables/
http://convergingontheedge.com/post/16916353412/mpls-primer-for-the-interested
http://www.wikipedia.org/
https://www.juniper.net/us/en/
http://www.cisco.com/
http://mellowd.co.uk/ccie/
http://blog.ioshints.info/